An electric current is the net movement of electric charge in a single direction.

A voltage difference is related to the force that cause charges to flow.

A circuit is a closed, conducting path.

Ohm’s Law:  current (flow) in amperes = voltage difference (in volts)                I=V/R

Resistance (in ohms)

- Create a simple series circuit with a power source, 1 light, wires and switch.  What happens when you close the switch?

- Add another light to the circuit.  Take note of what happens.  Then add a third light.  Describe what happens when you added these bulbs.

- Using Ohm’s Law above, describe what happened in step #2.

- Using a multimeter measure both the voltage and current with 3 lights working.  See illustration.   Then remove one light, and measure the voltage and current with 2 lights working.  Then do it with one light working.  Complete the data table below.  You need to Ohm’s Law to calculate the resistance of the lights.

| # of Lights | Voltage (V) | Current (Amps) | Resistance (Ohms) |
| --- | --- | --- | --- |
| 1 |  |  |  |
| 2 |  |  |  |
| 3 |  |  |  |

- Create a parallel circuit with a power source, 2 lights, wires and switch.  See the illustration below.  Measure voltage and current again.  The Data for one light is the same as it is above for one light.

| # of Lights | Voltage (V) | Current (Amps) | Resistance (Ohms) | Brightness of Light |
| --- | --- | --- | --- | --- |
| 1 |  |  |  |  |
| 2 |  |  |  |  |
| 3 |  |  |  |  |

- Electromagnet:

Remove all the lights and put them away.  Wire the coil, switch, wires and power supply into a single circuit.  As the teacher changes the voltage supplied to the circuit, record the voltage and the mass of the object (in grams) that the electromagnet can lift.

| Voltage (V) | Mass (g) |
| --- | --- |